## Slide 1: Compton polarimetry for SuperKEKB: Synchronisation
Aurélien MARTENS

## Slide 2: Introduction
Reminder:
  We have draw a conceptual design with excellent expected performance
  Design relies on:
Laser:
  Integrated in accelerator: must be fully remote operated
  Operated at frequency of 250MHz: must be well synchronized to accelerator RF
  Typical acceptable time jitter of ~500fs (a small fraction of electron bunch/laser pulse durations
Detector:
  photon calorimeter able to cope with photons incoming every 4ns.
  The 2500 circulating bunches measured independently
  Ability to provide fast on-line info to the control room
  Embedded electronics, fast enough, with good ADC (10 bits min) and FPGA processing
  With bunch identification

## Slide 3: Conceptual acquisition chain
BaF2
PMT
Optical filter
FPGA
IDROGEN board
White Rabbit node
Analog Front-end
+ ADC (>=10bits)
Every 4ns
2500 histograms
Fast treatment: fit
Accelerator RF
1rst Bunch identifier
To remote storage (10MB/min)
Reduced data
To online monitoring
clock
Update program, constants
Funding request in preparation for submission to ‘Agence Nationale de la Recherche’ for building and testing this detector with the electronics

## Slide 4: Laser synchronisation – concept
Master Oscillator (510MHz/51)
4km fibre link
IDROGEN, high speed DAQ
Low noise WR node
FPGA mezzanine card
WhiteRabbit
D. Charlet et al., https://cds.cern.ch/record/2893372?ln=en
H. Kaji, D. Charlet
WhiteRabbit allows to minimize implementation cost
A simple fibre to bring to the laser
No expensive/complicated fibre length compensation system to implement
Developments made in parallel at IJCLab and KEK:
IJClab:
  Standalone tests with phase noise measurements
  Test new developments on the IDROGEN board quickly
KEK:
  Test within KEK environment
  Possibility to test with 4km fibre loop easily
  Possibility to test accelerator/laser synchronisation  these two weeks at ATF

## Slide 5: Results
Measured at KEK, 4km fibre, June 2024
NB: 2m fibre gives the same result !
Rubidium
fibre link
8ps
1 ps
530 fs
160 fs
IJCLab, Sept. 2024
Improvement in configuration of PLLs
Degradation may be due to the measurement chain at IJCLab, TBC

## Slide 6: Next steps
Further developments made in parallel at IJCLab and KEK:
IJClab:
  Further improvements at low frequency may be possible  tests planned
  Ability to generate arbitrary frequency by integrating SI536x component
KEK:
  Test at ATF with laser
  Import improvements obtained at IJCLab and validate new perf
Synchronisation of laser (and data acquisition) is part of essential elements for the implementation of Compton polarimeter
  First tests made
  Working principle confirmed
  Performance is nearly met
  Still some residual phase noise contributions to understand
  Low frequency is more critical, planned laser technology is very stable at higher frequencies (>1kHz)