## Slide 1: Compton polarimetry for SuperKEKB: Synchronisation
Aurélien MARTENS
IJCLab

## Slide 2: Introduction
Reminder:
  We have draw a conceptual design with excellent expected performance
  Design relies on:
Laser:
  Integrated in accelerator: must be fully remote operated
  Operated at frequency of 250MHz: must be well synchronized to accelerator RF
  Typical acceptable (closed loop) time jitter of ~500fs (a small fraction of electron bunch/laser pulse durations
Detector:
  photon calorimeter able to cope with photons incoming every 4ns.
  The 2500 circulating bunches measured independently
  Ability to provide fast on-line info to the control room
  Embedded electronics, fast enough, with good ADC (10 bits min) and FPGA processing
  With bunch identification

## Slide 3: Conceptual acquisition chain
BaF2
PMT
Optical filter
FPGA
IDROGEN board
White Rabbit node
Analog Front-end
+ ADC (>=10bits)
Every 4ns
2500 histograms
Fast treatment: fit
Accelerator RF
1rst Bunch identifier
To remote storage (10MB/min)
Reduced data
To online monitoring
clock
Update program, constants
Funding request in preparation for submission to ‘Agence Nationale de la Recherche’ for building and testing this detector with the electronics
Proposal accepted for second stage of submission process  to be submitted on the 27th of March, result in June.

## Slide 4: Laser synchronisation – concept
Master Oscillator (510MHz/51)
4km fibre link
IDROGEN, high speed DAQ
Low noise WR node
FPGA mezzanine card
WhiteRabbit
D. Charlet et al., https://cds.cern.ch/record/2893372?ln=en
H. Kaji, D. Charlet
WhiteRabbit allows to minimize implementation cost
A simple fibre to bring to the laser
No expensive/complicated fibre length compensation system to implement
Developments made in parallel at IJCLab and KEK:
IJClab:
  Standalone tests with phase noise measurements
  Test new developments on the IDROGEN board quickly
KEK:
  Test within KEK environment for instance at ATF
  Possibility to test with 4km fibre loop easily (shown in Oct’24)
  Possibility to test accelerator/laser synchronisation  rescheduled for June at ATF

## Slide 5: Arbitrary frequency generation
Rubidium
fibre link
RF
Arbitrary frequency
Precision of 1 Hz, accuracy excellent (no drift over several hours)
Consistency of KEK and IJCLab measurements.
Identical phase noise for various different output frequencies
1.7ps RMS jitter [1Hz, 10MHz]
D. Charlet (IJCLab) et al., H. Kaji (KEK SKB),
K. Popov, A. Aryshev (KEK ATF)
Same configuration but two totally different qualification schemes

## Slide 6: Long term drift
D. Charlet (IJCLab) et al., K. Popov, A. Aryshev (KEK ATF)
Reference freq.
Generated freq.
X
X
split 50:50
split 50:50
Low Pass
Low Pass
~0.3degree RMS phase jitter (at 357MHz) i.e. 2.3ps RMS (below 1Hz)
NB: measurements made in a regular office, no thermal stabilization

## Slide 7: Next steps
Synchronisation of laser (and data acquisition) is part of essential elements for the implementation of Compton polarimeter
  Very encouraging results 2.4 ps RMS (<1Hz); 1.7ps RMS (>1Hz)
  Work ongoing to understand
    drift component of phase noise (temperature ?)
    Noise in intermediate region [1Hz, 100Hz]  White Rabbit protocol related ?
  Laser +accel synchro test not yet done (not possible in October)  June ‘25 at KEK ATF
  Integrate SI5362 chip on the IDROGEN board (avoid some spurs)
  Replace commercial switches by home made, well configured IDROGEN board (first results being analyzed)
  ADC mezzanine card at 1GHz prepared first tests being performed at IJCLab and KEK
  Possibility to measure absolute frequency with colleagues from metrology lab (SYRTE, Paris)
NB:
These results are only concerning the added jitter induced by the RF transport.
Electron beam jittering itself against absolute RF reference may be of similar scale already