## Slide 1: Compton polarimetry for SuperKEKB upgrade
Aurélien MARTENS

## Slide 2: Introduction
Description of the current best candidate for the location of the polarimeter
Open questions related to integration of the polarimeter that is made of 3 elements
  A laser-e beams interaction chamber
  A scattered electron detector
  A scattered photon detector

## Slide 3: Lattice around BLY magnets
Region of interest for laser-e interaction
Furtherest from the IP is better (less background)
e- beam ellipticity is not of major concern

## Slide 4: Beam pipe for interaction chamber
Belle2
We do not need these
Hera design
Similar design could be implemented:
What contraints on the tube ?
Probably need some shielding around the laser box (that needs to be thermalized)

## Slide 5: Photon detector location and needs
There seem to be enough space for a photon detector after BLY1LE.1 or BLY1LE.2
Blue lines are line of sights for photons scattered from IPs located right before these dipoles
A window in the e-beam pipe must be placed and a secondary tube installed to the photon detector (in air, thus a second window needed)
--> vacuum level requirement to be determined but probably 10-6mbar is already too good.
1m

## Slide 6: Electron detector location
https://jinst.sissa.it/LHC/TOTEM/ch04.pdf

## Slide 7: Questions
Do you a major issue to implement the polarimeter at this location ?
Any comment on these ideas of implementation ? In particular impedance-wise