## Slide 1: Some thougts about transverse polarimetry for the SuperKEKB upgrade
Aurélien MARTENS

## Slide 2: Introduction
The possibility of the phased approach of the upgrade has been mentioned
The first step would be do produce, transport and store polarized electron beams
A Compton polarimeter able to measure the transverse beam polarization would be nice (to actually show and quantify the polarization transport)
I try to look at this possibility today

## Slide 3: Compton cross-section
The Compton cross-section averaged over scattered particles spins:
Differential cross-section
Electron beam polarization independent
Electron beam polarization dependent
Transverse laser polarisation: nuisance parameter to minimize and keep under control
Transverse electron beam polarisation: intervenes as an asymmetry in the transverse plane
⚠️ Transverse e-beam polarimetry implies measuring geometrical asymmetries in the detection plane

## Slide 4: A first look at the unpolarized term
Landau-Lifshitz QED book paragaphs 86 and 87
Initial electron energy (7 GeV)
Initial photon energy (1.2eV at 1030nm)
Crossing angle of beams
Emitted photon energy
Conical emission:
98% of photons within 730𝜇rad
laser (Eλ)
θ
e- beam
energy vs emission angle correlation
⚠️ Photons (electrons too) are scatterred in the forward direction, in a narrow cone around the electron beam axis
Typical opening:
1/gamma~70urad
Typical spatial resolving power:
7mm for a detector at 100m

## Slide 5: Some history
Material taken from: https://indico.cern.ch/event/1181966/contributions/5046178/attachments/2512013/4318517/220905_tpol.pdf
Exactly the operation that was done at HERA TPOL a long time ago.
Notoriously a difficult task but ‘do-able’
Can be eased by implementing a nicely vertically segmented electron detector.
 Requires detailed simulations

## Slide 6: SuperKEKB implementation
We typically need a long line of sight for the photon beam ~50-100m
There are not so many places for that in SuperKEKB ring…
One option could be somewhere around FUJI
FUJI
Laser-e beam IP ?
Detector somewhere here ?
Positron injection  radiation levels in laser system…
Thanks to D. Zhou and M. Masuzawa for the help, pics…
~100m
It sounds that the environment will be harsh for the laser (at least…)

## Slide 7: Magnet…
BX1E magnet is 5.9m length, the outcome is similar to that around BLA2LE
Magnet modification is required to let the photon beam out.

## Slide 8: Electron detector
Not so much space. Need to discuss its possible integration

## Slide 9: Alternative: BLA2LE/BLX2LE.2
Line of sight ~20-30m provided that fence can be moved and something placed in between the two arcs
 Requires some very detailed simulation to prove the concept works
But same location of laser as final polarimeter, photon detector needs to be moved ‘as far as possible’
Requires a detailed look, on site.
Still need to change magnet… (for the photon detector)
Probably need move/change 1rst quad
BLA2LE
Laser/e-beam interaction point
Photon detection
Electron detection

## Slide 10: Conclusion
Insertion of transverse Compton polarimeter is not a straightforward step in the upgrade
  maybe a new polarimeter in a new location
  or recycle location proposed earlier for L-polarimeter
Magnet modification to let gamma beam out
  In any case required
  Not a cheap operation, lattice change  needs to be studied
Integration for electron detector
  Might be possible  need some evaluations
Photon detector requires detailed simulations