## Slide 1: Update about Compton polarimeter at SuperKEKB
Farah MAWAS
Aurélien MARTENS

## Slide 2: Introduction
A summary and update of IJCLab activities has been presented yesterday at Hiroshima Workshop by Farah and Aurelien.
https://indico.belle2.org/event/7500/timetable/#20230209.detailed
We give here some summary:
polarimeter integration
sensitivity studies for photon detector
Some comments about transverse polarimetry and Touschek lifetime

## Slide 3: BLA2LE/BLX2LE.2
BLA2LE
Laser/e-beam interaction point
Photon detection
Electron detection

## Slide 4: Mechanical system integration
450 mm
910 mm
Cross Angle Horizontal : 10 deg
Cross Angle Vertical : 4 deg
May need some lead shielding around electronics to be located below the table

## Slide 5: Toy-MC sensitivity studies
We focus on photon detection here
We simulate e-/laser interaction extract
For the fit:
Fixed parameters: e- beam energy and spread, , ,
Free parameters: , miscalibration scale, relative scale of each contribution (1 or 2 Compton photons), detector energy resolution

## Slide 6: Statistical sensitivity
(%)
Acquistion time (min)
For 25 min, there’s 0.5% error on the extraction of
For 1 min, there’s 2.2% error on the extraction of

## Slide 7: Signal+background Toy-MC
!!
Background fitting being worked on.
Significant bias of the fit with background included
~0.45% systematic uncertainty assigned
Actual background need to be measured to improve significance of simulation

## Slide 8: Table of systematics
Need to add a systematic uncertainty associated to mis-knowledge of laser polarization
~0.3% at most, target 0.1%
Systematic uncertainty related to transport of polarisation from Compton IP to Belle 2 ?

## Slide 9: Transverse polarimetry at HERA
Exactly the operation that was done at HERA TPOL a long time ago.
Notoriously a difficult task but ‘do-able’
Eased by implementing a nicely vertically segmented electron detector.
Requires detailed simulations
Requires some transverse sampling (not easy for photons)
https://indico.cern.ch/event/1181966/contributions/5046178/attachments/2512013/4318517/220905_tpol.pdf

## Slide 10: Touschek lifetime can be used also
Touschek described the lifetime of electrons in AdA (’accumulation ring’) in 1963 (Bernardini et al., Phys. Rev. Lett 10 (1963) 407)
Baier & Khoze, pointed out that Touschek lifetime is sensitive to polarization (At. Energ. 25 (1968) 440)
It was then use in the VEPP-2M ring to measure depolarization (and thus beam energy): Derbenev Part. Acc. 8 (1978) 115
  Measuring the couting rate of scattered electrons
Ex: Allowed first precision mass measurement of J/Psi (3096.93+-0.09 MeV) then superseded in 1993 (E760)
Continously improved at VEPP-4M (KEDR at VEPP-4M: 3096.900 ± 0.002 ± 0.006 MeV): Phys. Lett 96B (1980) 214; Blinov et al., proc. of EPAC (2002) 1954

## Slide 11: a slightly more modern use
Used at :
  HIgS (DUKE): NIMA 614 (2010) 339
  SOLEIL, NIMA 697 (2013) 1
  Diamond Light Source, PRAB22 (2019) 122801
  Based on expressions given in NIMA 554 (2005) 85
  Also proposed for FCCee: arXiv1909.12245

## Slide 12: For SuperKEKB
It is ~4% effect assuming (overall) momentum acceptance of 0.6%, and using her_2021-06-09_231636.388_MeasOpt
This is likely observable in SuperKEKB
May need to inject both polarized and unpolarized beams in the ring and measure bunch/bunch intensity with time to minimize systematics (feasbile according to Demin)
Maybe F/C factor could be calibrated by comparing measurements with various momentum acceptances ? (linked to RF voltage ?)

## Slide 13: Conclusion
Laser interaction chamber integration has progressed well
Sensitivity studies for photon detector nearly completed for a CDR document
Transverse polarimetry could be done with Touschek lifetime or with HVMAPS of Manitoba, more difficult for photon detector
Real-time laser polarimetry being worked on (some progresses already)
Next steps:
  Photon detector integration concept (need tunnel visit next week).
  Improve optics design
  CDR document
  Prototype BaF2 detector (needs funding : just got answer from French national agency that not selected for 2023)